## Slide 1
Install, maintain and test hardware in a technology system.
Install and maintain hardware in the technology system.
In order to fulfil the client's requirements, we will install and maintain hardware components in the technology system of West Mercia Employment. Based on the action plan, we will focus on two internal components and one additional external hardware device.
Internal Component 1: RAM Upgrade
  Using appropriate tools, such as a screwdriver and an antistatic wristband, we will open the computer casing.
  Identify the existing RAM module and remove it carefully.
  Install the new RAM module in the available slot, ensuring it is securely seated.
  Close the computer casing and ensure all connections are properly reattached.
Training and installing video:
How to Install RAM into a Desktop PC (2023) - YouTube
Internal Component 2: Solid State Drive (SSD) Installation
  Open the computer casing following safety precautions.
  Locate the existing hard disk drive (HDD) and disconnect it from the power and data cables.
  Insert the new SSD into an available drive bay and secure it using screws.
  Connect the power and data cables to the SSD, ensuring a secure connection.
  Close the computer casing and verify all connections.

## Slide 2
Training and installing video:
How to install an SSD - Step By Step Setup Guide and Windows 10 Install - YouTube
Additional External Hardware Device: Network Printer Setup
  Connect the network printer to the network using an Ethernet cable.
  Install the necessary printer drivers on the client computers.
  Configure the network printer settings, such as IP address and shared permissions.
  Test the printing functionality from multiple client computers.
Training Video:
How to set up printer for a network (01) - YouTube
Protect data and system settings during hardware maintenance.
To protect the data and system settings during hardware maintenance, we will follow best practices and use appropriate tools and techniques to safely back up the data before making any modifications to the technology system. We will also ensure the safe restoration of the data and system settings after the modifications are completed.

## Slide 3
Data Backup:
  Prior to making any modifications, we will use a reliable backup software to create a complete backup of all relevant data, including client records, communication files, and system configurations.
  The backup will be stored securely on an external storage device or a cloud-based solution to ensure data integrity and availability.
System Settings Restoration:
  After the modifications are completed, we will restore the system
settings by utilizing the backup created earlier.
  We will carefully follow the instructions provided by the backup software to ensure a smooth and accurate restoration process.
  Verifying the restored system settings will be done to ensure that all
configurations and preferences are correctly applied.
*By following these procedures, we demonstrate good practice in protecting data and system settings during hardware maintenance, minimizing the risk of data loss or system instability.
Test functionality and troubleshoot hardware faults.
During the testing phase, we will evaluate the functionality of the modified technology system, identify any technical difficulties, and troubleshoot and repair internal hardware faults as necessary. We will also document any issues encountered and the steps taken to resolve them.
1. Testing for Functionality:

## Slide 4
Using the test plan developed earlier, we will execute various tests to ensure the modified system meets the specified requirements.
We will test features such as client data maintenance, communication systems, and the provision of relevant information to customers.
Detailed test logs will be maintained, documenting the test methods,
expected results, actual results, and any further actions required.
Training video:
PC Troubleshoo�ng: Basic Troubleshoo�ng Techniques - YouTube
Troubleshooting and Repair:
  If technical difficulties arise during installation and maintenance, we will employ appropriate troubleshooting techniques to identify the root causes of the issues.
  Fault-finding tools will be utilized to diagnose and repair any internal
hardware faults encountered.
  We will document the difficulties faced, the troubleshooting steps
taken, and the solutions implemented to resolve the issues.
Test system functionality, data backup, and gather user feedback.
To ensure the system functions as intended and provide an optimal user experience, we will conduct thorough testing, including data backup and restoration verification. Additionally, we will gather user feedback through a questionnaire to assess the usability and user experience of the modified system.
1. Testing System Functionality and Data Backup:

## Slide 5
Execute a series of test scenarios based on the original requirements and modifications made.
Record the test method used, expected results, actual results, and
note any further actions required.
Specifically test the data backup process, ensuring that data is
securely backed up and can be restored successfully.
User-Experience Testing and Feedback Gathering:
  Prepare a questionnaire to gather feedback from the designated
"client" or end-users.
  The questionnaire should cover aspects such as ease of use, clarity of instructions, speed, and overall satisfaction with the modified system.
  Guide the "client" through the system, observing their interactions and recording their feedback.
- Document the feedback received in the form of a table or written record.
Training video:
Backup and Recovery Best Prac�ces - YouTube
Enabling Backup & Recovery Best Prac�ces in 2021 with Rubrik - YouTube
Refine the system for improved performance and
customization.
Based on the test results, feedback, and customization requirements, we will refine the system to improve its performance and customize it to suit the client's needs. This iterative process may involve adjusting hardware

## Slide 6
settings, customizing advanced features of components and devices, and cleaning internal components to prevent overheating.
Performance Refinements:
  Review the test results and identify areas for improvement, such as system responsiveness, data processing speed, or user interface optimization.
  Implement necessary changes to enhance performance, such as adjusting hardware configurations, optimizing software settings, or upgrading components if required.
  Document the refinements made and describe the benefits they bring to the user, such as improved efficiency, faster data access, or smoother workflow.
Customization and Advanced Settings:
  Explore the advanced settings of hardware components and external
devices, such as printers or networking equipment.
  Customize these settings to maximize their capabilities and tailor
them to the client's specific requirements.
  Examples of customization may include adjusting print quality settings, optimizing network performance, or enabling specific features offered by the devices.
  Document the customized settings and explain how they enhance usability and fulfil the client's needs.
Cleaning Internal Components:
  Recognize the importance of maintaining a clean and dust-free system to prevent overheating and component failure.
  Demonstrate the process of cleaning internal components, such as power supply units and CPU heatsinks, using appropriate tools and techniques.

## Slide 7
- Emphasize the benefits of regular cleaning in improving system stability, prolonging hardware lifespan, and reducing the risk of overheating-related issues.

## Slide 8
Service Level Agreements (SLAs):
In situations where a company leases its computer system from a supplier, it is common to have a service level agreement (SLA) in place. This agreement outlines the terms and conditions between the company and the supplier regarding the use and performance of the computer system. One important aspect of the SLA is the guarantee of 100 percent system availability provided by the supplier to the company. This means that the supplier commits to ensuring uninterrupted use of the systems, and failure to meet this guarantee may result in penalties for the supplier.
Furthermore, if the supplier identifies a fault with a component in the computer system, they are obligated under the SLA to quickly upgrade or replace the faulty component with a similar one. This prompt action is taken to minimize any negative impact on the company's operations and to maintain the smooth functioning of their business activities.
Overall, service level agreements play a crucial role in defining the responsibilities, expectations, and consequences for both the company and the supplier in ensuring the reliable and efficient operation of the leased computer system.

## Slide 9
Risks during hardware installation:
Potential damage to equipment can occur when removing a component from a computer system. It is crucial to handle the equipment gently and safely to minimize the risk of causing any harm. Mishandling can lead to various forms of damage, such as overtightening screws and stripping the threads, accidentally dropping components, bending pins in plugs or sockets, or loosening cables in plugs. To mitigate these risks and prevent damage, it is important to exercise caution and remove the equipment slowly and carefully.
Electrostatic discharge (ESD):
Electrostatic Discharge (ESD) refers to the sudden transfer of electricity from one object to another. This phenomenon can be observed in various situations, such as when lightning occurs, when you experience a shock after jumping on a trampoline and then touching a pole, or when crackling and sparks appear while removing clothes from a dryer. ESD typically arises when two objects come into contact, rub against each other, slide, or separate. The concerning aspect is that ESD can cause damage to components even without immediate detection. A seemingly imperceptible charge or electricity can be as detrimental to components as a powerful lightning bolt. Given that modern components are smaller, more efficient, and thus more delicate and sensitive to ESD than before, it is crucial to follow three guidelines for prevention. Firstly, it is essential to assume that all components and assemblies are sensitive to ESD. Secondly, when handling ESD-sensitive items, ensure that you are properly grounded within a static-safe work area. Lastly, when storing and transporting ESD-sensitive items, it is recommended to utilize static shielding containers. By adhering to these rules, the risk of ESD-related damage can be significantly minimized.​

## Slide 10
Component damage:
Inadequate handling of hardware components can result in physical damage. When ICT professionals fail to adhere to safety rules and jeopardize the integrity of hardware components, it can lead to significant issues and pose obstacles during the process of upgrading the components. To prevent physical damage to devices and cabling, it is imperative to exercise caution when performing computer system upgrades and diligently follow all safety rules. One of the most critical rules is to utilize appropriate tools that help mitigate risks associated with component damage. By taking meticulous care and using the right tools, the potential for harm can be minimized.​
Risk of Data:
1- Data loss and corruption:
During the process of upgrading hardware components, particularly the hard drive, data loss and corruption are common issues. It is possible to lose data or render it unusable by damaging or formatting the hard disk. Although data recovery is feasible, it is a costly and time-consuming endeavour. Therefore, the most effective approach is to prevent data loss altogether. Data corruption occurs when certain files are altered or damaged, rendering them unreadable even though they still appear in the system. To safeguard your data, it is recommended to back up your computer system. This entails creating a duplicate copy of your data. The best practice is to adhere to the "3-2-1 rule," which involves having three copies of your data stored on two different types of storage devices, with one copy stored off-site or in the cloud. To facilitate real-time backups and cloud storage, software like Back blaze can be utilized.​

## Slide 11
2-Service loss:
Service loss refers to situations where service providers experience disruptions, such as the loss of internet connection, which are not caused by the user's error or computer system issues. While it is impossible to prevent service loss entirely, many companies have customer services in place to assist in resolving such problems remotely or by sending technicians to the customer's location for necessary repairs. These customer service measures aim to address and rectify service disruptions promptly and efficiently.

## Slide 12
Checking health and safety regulations:
"When installing hardware, it is essential to adhere to health and safety regulations to ensure a safe working environment. This includes promptly reporting any accidents that may occur, taking necessary precautions for personal health and safety when handling heavy components, avoiding electrical hazards, and ensuring that workstations meet safety requirements. Compliance with these regulations is crucial as they help prevent any potential harm or injuries to oneself or others in the vicinity. ICT professionals have a responsibility to safeguard both themselves and the working area while performing tasks related to computer systems.“
To avoid accidents, several safety rules should be followed:
1. Maintain a clean and tidy work area.
2. Always unplug the computer before conducting any upgrades.
3. Use appropriate tools suitable for the task at hand.
4. Do not keep any drinks near the work area.
5. Wear an ESD band and use an anti-static mat while upgrading hardware components.
6. Refer to a checklist to ensure nothing is overlooked.

## Slide 13
Utilization of antistatic equipment:
It is crucial to consistently employ any antistatic equipment provided, including:
1. Antistatic packaging.
2. Wrist straps.
3. Antistatic mats.
If none of these equipment options are available, it is important to inquire about their absence and whether they can be provided. This inquiry helps ensure that proper precautions are in place to mitigate the risks associated with electrostatic discharge and safeguard sensitive components during hardware installation or handling.
​

## Slide 14
Anti-static packaging:
Anti-static packaging is designed to safeguard components during transportation. It is a specialized type of plastic bag that incorporates shielding within the material to prevent the build-up and discharge of static electricity. By utilizing anti-static packaging, the contents of the bag are shielded from potential damage caused by electrostatic discharge.
Anti-static wrist strap:
An anti-static wrist strap is employed to dissipate static electricity from the wearer's body. It consists of a band that fits around the wrist, connected to a cable that must be grounded to an appropriate earth connection. Typically, a specialized mains plug with a connector for the cable is used. The cable includes a resistor to provide additional protection. It is important to ensure that the cable is properly connected to the grounding point for the wrist strap to effectively discharge any static electricity and prevent potential damage to sensitive components.
Anti-static mats:
Anti-static mats serve to protect components during work processes. They are commonly placed on workbenches and used as a resting surface for components during system dismantling or assembly. For the anti-static mat to be effective, it must be properly connected to an earth ground. This connection ensures that any static charges generated on the mat are effectively dissipated, minimizing the risk of electrostatic discharge and potential damage to the components.

## Slide 15
Installing and maintaining hardware in a PC can be challenging and can having weaknesses:
Hardware components can be expensive to replace if they become damaged. Certain high-performance components like Graphics Cards can have a substantial cost, reaching up to £1000. It is important to handle them with care to avoid any accidental damage.
Compatibility is a crucial factor when it comes to hardware and motherboards. Not all hardware is compatible with every motherboard, and in such cases, professionals might be required to make the necessary adjustments. Hiring professionals for compatibility-related tasks may involve additional costs.
During the maintenance or installation of new hardware, there is a possibility of overlooking certain connections. Failing to connect all the necessary components properly can result in the computer not functioning as intended. It is essential to double-check all connections to ensure everything is properly linked.
The presence of numerous wires in a computer system can create hazards if they are not managed safely. The abundance of wires can make it challenging to maintain proper organization and ensure that all equipment is securely in place and appropriately connected. Mishandling the wiring can potentially lead to damage to the hardware components.
It is advisable to minimize excessive movement of the computer system. When devices are plugged into a power socket, there can be a surge of electricity for a brief period before it stabilizes. Frequent movement of the computer system and repeated connections can increase the likelihood of a power supply unit (PSU) failure or other hardware damage. It is important to keep the computer system in a stable position to avoid such risks.

## Slide 16
Tools Required and Recommended for PC Hardware Installation and Maintenance:
Hand Tools:
1. Flathead screwdriver (large and small)
2. Phillips-head screwdriver (large and small)
3. Tweezers or part retriever
4. Needle-nosed pliers
5. Wire cutters
6. Chip extractor
7. Hex wrench set
8. Atrox screwdriver
Miscellaneous Tools:
- SSD jumpers
- Case screws
- SSD screws
- Case thumbscrews
Diagnostic Tools:
- Digital multimeter
- Loopback adapter
- Toner probe
These tools are essential for various tasks involved in PC hardware installation and maintenance, including screwing and unscrewing components, handling small parts, cutting wires, extracting chips, and diagnosing hardware issues. It is recommended to have these tools readily available to ensure smooth and efficient hardware-related tasks.